## Slide 1: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
Reason
  L1 = 4K DWORD = 4BANK
  1 BANK = 1K DOWRD = 16 DWORD(width) * 64(depth)
  address[7:6] select which bank
  address[5:0] select inner one bank
  Cacheline = 16DWORD = bank width

## Slide 2: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
Best practice
  cacheline usage = 100%
  Every 16 thread has no bank conflict,
    that means one wave cover 4 bank
    also means address[7:6] should range from 00b to 11b within one wave

## Slide 3: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dword with cacheline usage = 100%
  Every continues 16 thread read one entire cacheline
  No bank conflict
  No block, every 4 clk per issue

## Slide 4: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dword with cacheline usage = 1/16
  Every continues 16 thread read one entire cacheline
  Every 16 thread has bank confilict
  64 clk per issue after first 12 issue

## Slide 5: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4 with cacheline usage = 100%, no bank conflict
  Every continues 4 thread read one entire cacheline
  Every continues 16 thread cover 4 banks
  16 clk per issue after first 12 issue

## Slide 6: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4 with cacheline usage = 100%, with bank conflict
  Every continues 4 thread read one entire cacheline
  Every continues 16 thread cover only 2 banks, 2 bank conflict
  32 clk per issue after first 12 issue

## Slide 7: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4 with cacheline usage = ¼, with bank conflict
  Every thread read different cacheline
  Every continues 16 thread cover only 1 banks, 4 bank conflict
  64 clk per issue after first 12 issue