## Slide 1: VMEM PERFORMANCE
ISSUE BLOCKING DUE TO SQ BUFFER
Reason
  12-depth Instruction buffer per cu (TA?)
  wait TA send back req-ack, then release
  TA req takes 4 address token,
  one token takes 4 continues address data(dword)
flat_load_dword
  cacheline usage 100%: not block
  cacheline usage<100%: first 12 issue not block
flat_load_dwordx4
  only first 12 issue on the cu will not block
  that means if we have 4 wave in one cu, we should only issue 3 flat_load_dwordx4 at most per thread to avoid issue blocking