## Slide 1: DPP FOR FFT
Environment：
  Vega20 60 cu
  Data type = float2
  FFT length = 2048
  Group size = 1024
  4 wave per SIMD; 16 wave per CU
Method:
  1 origin
  2 dpp
  3 dpp with twiddle in lds
  4 dpp with twiddle in flight

## Slide 2: DPP FOR FFT
Method 1: origin
  Use lds-sync to do data exchange
Method 1

## Slide 3: DPP FOR FFT
Method 1: origin
  need to wait global read and lds read/write opt are finished (not good)
  Another wave could use VALU while one wave is waiting (good)
Method 1
load twiddle
read x from lds
write result to lds
wait read complete
wait write complete
656 clk

## Slide 4: DPP FOR FFT
Method 2: dpp
  Increase another 8 dpp and cndmask instructions : 32 clk
  No need to sync
Method 2

## Slide 5: DPP FOR FFT
Method 2: dpp
  Only need to wait reading twiddle from global mem (good)
  Compiler will generate lots of condition branch instructions (compiler issue)
  One wave will holding VALU during butterfly calculate, can’t interleave with other wave(not good)
Method 2
948 clk
load twiddle
lots of condition
butterfly
Wait load twiddle complete

## Slide 6: DPP FOR FFT
Method 2: dpp
  One wave will holding VALU during butterfly calculate, can’t interleave with other waves well (not good)
Method 2
Waiting other waves
Waiting global load

## Slide 7: DPP FOR FFT
Method 3: dpp with twiddle in lds
  Compiler can’t generate correct code, only work with –O0 (compiler issue)
  Only read from lds, so no need to sync
Method 3

## Slide 8: DPP FOR FFT
Method 3: dpp with twiddle in lds
  Lds_read, S_waitcnt , valu instructions in wrong orders (compiler issue)
  Different waves could interleave, better than origin method (good)
Method 3
208 clk
read twiddle from lds
butterfly

## Slide 9: DPP FOR FFT
Method 4: dpp with twiddle in flight
  Use double precision to calculate phase
  Use v_cos/sin_f32 instruction to calculate twiddle
Method 4

## Slide 10: DPP FOR FFT
Method 4: dpp with twiddle in flight
Method 4
butterfly
840 clk
Calculate twiddle
Condition

## Slide 11: DPP FOR FFT
Method 4: dpp with twiddle in flight
  One wave will holding VALU during butterfly calculate, can’t interleave with other waves at all (not good)
Method 4
Waiting other waves

## Slide 12: DPP FOR FFT
Conclusion ：
  Use dpp with load twiddle in lds (if we could avoid compiler issue)
    It has fewer instructions
    Different wave could interleave while waiting for lds_read