## Slide 1: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
Reason
  L2 = 1M DWORD = 16 channel
  1 channel = 64K DOWRD = 64 DWORD(width) * 1024(depth)
  address[11:8] select which channel
  1 arbiter per channel
    round robin
    2 request per clk
  Bandwidth:
    64 DWORD for one CU
    64 DWORD*16 channel
    = 1024 DWORD / clk
TCPn
Req
fifo
arbiter
mux
TCPn
Req
fifo
TCCn

## Slide 2: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
flat_load_dwordx4
  channel usage = 100%
  1 cu per channel, 16 groups cover 16 channel
  4 clk for 12 issue
  16 clk for 19 issue
  32 clk for 12 issue
  64 clk for after

## Slide 3: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
flat_load_dwordx4
  channel usage = 100%
  2 cu per channel, 32 groups cover 16 channel
  4 clk for 12 issue
  16 clk for 18 issue
  32 clk for 7 issue
  block for after

## Slide 4: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
flat_load_dwordx4
  channel usage = 100%
  total 16 groups
  1 groups cover 16 channel. (256 thread per group, 4 dword per thread)
  4 clk for 12 issue
  16 clk for after

## Slide 5: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
flat_load_dwordx4
  channel usage = 100%
  total 32 gourp
  1 groups cover 16 channel. (256 thread per group, 4 dword per thread)
  4 clk for 12 issue
  16 clk for 19 issue
  Random block

## Slide 6: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
flat_load_dwordx4
  channel usage = 100%
  all groups access only one channel
  4 clk for 12 issue
  16 clk for 12 issue
  Random block after (about 500 clk)

## Slide 7: VMEM PERFORMANCE
Issue blocking due to l2 channel conflict
Best practice
  Channel usage = 100%
  One group cover 16 channel per instruction