## Slide 1: VMEM PERFORMANCE
ISSUE BLOCKING DUE TO SQ BUFFER
Reason
  12-depth Instruction buffer per wave
  wait TA send back req-ack(not data back), then release
  TA req takes 4 address token, one token takes 4 continues address data(dword)
  So if 4wave/cu, flat_load_dwordx4, best coalescing
    4 thread per req
    1 wave = 64 thread = 16 req = 16 clk

## Slide 2: VMEM PERFORMANCE
ISSUE BLOCKING DUE TO SQ BUFFER
flat_load_dword
  cacheline usage 100%: not block
  cacheline usage<100%: first 12 issue not block
flat_load_dwordx4
  only first 12 issue on the cu will not block
  that means if we have 4 wave in one cu, we should only issue 3 flat_load_dwordx4 at most per thread to avoid issue blocking