## Slide 1: VMEM PERFORMANCE
Cache
topology
  /sys/devices/virtual/kfd/kfd/topology/nodes/[nodeIdx]/caches/[cacheIdx]
  total cache count = 96
    64 L1 data cache, size = 16KB
    16 instruction cache, size = 8KB
    16 constant data cache, size = 4KB
CU0
CU1
CU2
CU3
L1 cache
L1 cache
L1 cache
L1 cache
Instruction cache
constant cache
L2 cache
HBM
BUS

## Slide 2: VMEM PERFORMANCE
cache
L1 data cache
  L1 = 4K DWORD = 4BANK
  1 BANK = 1K DOWRD = 16 DWORD(width) * 64(depth)
  Bandwidth L1 -> CU = cacheline / clk = 16 DWORD / clk
  address[13:12] select which bank, address[11:6] select cacheline
  Cacheline = 16DWORD = bank width

## Slide 3: VMEM PERFORMANCE
Cache
  Get cacheline_idx from addr[cachelineIdx]
  Get cacheline from cache by cacheline_idx
  Check valid bit in cacheline
  Get tag from cacheline
  Compare tag with addr[tag]
Hit & miss

## Slide 4: VMEM PERFORMANCE
Bank 0
Bank 1
Bank 2
Bank 3
tag
cacheline
Cache
4 way set
  Reduce hardware usage
  Reduce tag compare time

## Slide 5: VMEM PERFORMANCE
Cache
L1 update policy
  Write through: when sp write, if addr hit in L1, we update the data in L1 as well as data in L2, when sp read the addr after , it always gets the latest data

## Slide 6: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dword with cacheline usage = 100%
  Every continues 16 thread read one entire cacheline
  No bank conflict
  No block, every 4 clk per issue

## Slide 7: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dword with cacheline usage = 1/16
  Every continues 16 thread read one entire cacheline
  Every 16 thread has bank confilict
  64 clk per issue after first 12 issue

## Slide 8: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 100%, every continues 4 thread read one entire cacheline
  bank usage = 100%, every continues 16 thread cover 4 banks
  16 clk per issue after first 12 issue

## Slide 9: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 100%, every continues 4 thread read one entire cacheline
  bank usage = 50%, every continues 8 thread cover only 2 banks
  32 clk per issue after first 12 issue

## Slide 10: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 100%, every continues 4 thread read one entire cacheline
  bank usage = 25%, every continues 4 thread cover only 1 banks
  64 clk per issue after first 12 issue

## Slide 11: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 50%, every continues 2 thread read half cacheline
  bank usage = 100%, every continues 8 thread cover 4 banks
  32 clk per issue after first 12 issue

## Slide 12: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 25%, every thread read 1/4 cacheline
  bank usage = 100%, every continues 4 thread cover 4 banks
  64 clk per issue after first 12 issue

## Slide 13: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4
  cacheline usage = 50%, every continues 2 thread read half cacheline
  bank usage = 50%, every continues 4 thread cover 2 banks
  64 clk per issue after first 12 issue

## Slide 14: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
 |  | Bank usage |  | 
 |  | 100% | 50% | 25%
cacheline usage | 100% | 16 clk | 32 clk | 64 clk
 | 50% | 32 clk | 64 clk | 64 clk
 | 25% | 64 clk | 64 clk | 64 clk
flat_load_dwordx4
Other pattern

## Slide 15: VMEM PERFORMANCE
Data return latency
Data return
  1 wave per cu, flat_load_dwordx4 then waitcnt(0)
  Total read = 4 DWORD * 64 thread = 256 DWORD
  Theoretic elapsed = 256 / 16 = 16 clk
  Data return in 184 clk
  Latency = 168 clk

## Slide 16: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
flat_load_dwordx4 with cacheline usage = ¼, with bank conflict
  Every thread read different cacheline
  Every continues 16 thread cover only 1 banks, 4 bank conflict
  64 clk per issue after first 12 issue

## Slide 17: VMEM PERFORMANCE
Issue blocking due to l1 bank conflict
Best practice
  cacheline usage = 100%
  Every 16 thread has no bank conflict,
    that means one wave cover 4 bank
    also means address[7:6] should range from 00b to 11b within one wave
  2 issue per wave after s_barrier
  10 issue per wave after s_waitcnt